Linux Kernel Module Programming
Arş. Grv. R. Can AYGÜN

---
Outline
- Linux Kernel
- Kernel Modules
- Device Drivers
- Parallel Port Device Driver Implementation

---
Linux Kernel
- Monolithic kernel, Preemptive scheduling
- But not a static kernel like the traditional monolithic kernels. Device drivers can be load to kernel as “Module”.
- Abstraction of underlaying hardware
- File system management, CPU scheduling, memory management, Networking, Security

---
Linux Kernel

---
Kernel Module
- Modules are pieces of code that can be loaded and unloaded into the kernel upon demand
- Extents the kernel functionality
- No reboot required to use new functionality
- Loadable kernel modules can be device drivers,additional file system supports and new system calls

---
Kernel Module ~ Operations
- List running modules → lsmod
- Insert a module to kernel → insmod or modprobe
- Delete a module from kernel → rmmod

---
Device Driver
- A driver is the part of the OS that manages communication with devices.
- Peripheral or internal devices allow users to communicate with the computer.
    - keyboards, monitors, floppy and hard disks, CD-ROMs, printers, mice (serial/parallel), networks, modems, etc.

---
Device Drivers
Character Device Drivers:
- Write and read operations are done char by char
- Works in Blocking Mode; write and wait, synchronously
  such as; LPT printer
  Block Device Drivers:
- Write and read → block by block
- Working in Asynchronous mode.
  Such as; usb drives, mouse

---
Device File
Interface between user space and kernel
User space applications can only access device via device file
Device files are placed in /dev directory
A major and minor number must be assigned to any device file.

---
Parallel Port Char Device Driver
Implementation
Output of the parallel port will be showed via led lambs.

---
Parallel Port Pin Out

---
Breadboard Setup - 1

---
Breadboard Setup - 2

---
Parallel Port Device Driver Implementation Steps :
Steps :
- Writing the module code
  - Creating a make file which includes kernel libraries to compile the code as loadable kernel module
Check parallel port availability → cat proc/ioports (parallel port – ioport number: 0x378 )
- Add to blacklist other drivers which use the parallel port(if it is necessary).
  - /etc/modprobe.d/parport_pc.conf
  - Edit parport_pc.conf's inside as “blacklist parport_pc”
  - Restart the computer
- Create device file → mknod dev/parlelport c 61 0
Give permissions to device file chmod 666 /dev/parlelport
- İnstall our module to kernel → insmod pardrive.ko
- Check if our module controls the parallel port or not ?
  - cat proc/ioports
- Testing:	echo –n A >/dev/parlelport

---
References
- http://tldp.org/LDP/lkmpg/2.6/html/
- http://www.tuxradar.com/content/how-linux-kernel-works
- http://www.linuxjournal.com/article/7353?page=0,1
- http://matthias.vallentin.net/blog/2007/04/writing-a-linux-kernel-driver-for-an-unknown-usb-device/
- http://www.jespersaur.com/drupal/book/export/html/21
- http://d4web.net/sths/TEJ/U04Interfacing/A01Parallel/parallelPort.html