## Slide 1: Robot Teknolojisine Giriş Yrd. Doç. Dr. Erkan Uslu, Doç. Dr. Sırma Yavuz, Doç. Dr. Fatih Amasyalı, Ar. Grv. Nihal Altuntaş, Ar. Grv. Furkan Çakmak D011 Cuma 14:00-17:00 04

## Slide 2: Sensors for Mobile Robots
SENSING
PLANNING
ACTING
information
about the
environment
action
on the
environment

## Slide 3: Why Do Robots Need Sensors?
What is the angle of my arm?
internal information

## Slide 4: Why Do Robots Need Sensors?
Where am I?
localization

## Slide 5: Why Do Robots Need Sensors?
Will I hit anything?
obstacle avoidance

## Slide 6: Why Do Robots Need Sensors?
Sensing for specific tasks
Where is the cropline?
autonomous harvesting

## Slide 7: Why Do Robots Need Sensors?
Sensing for specific tasks
Where are the forkholes?
autonomous material handling

## Slide 8: Why Do Robots Need Sensors?
Sensing for specific tasks
Where is the face?
face detection & tracking

## Slide 9: Sensor Classification
Proprioceptive
  Measures robotic interaction with environment
  GPS, INS (inertial navigation system), shaft encoder
Exteroceptive
  Measures environment directly
  Contact, range, vision sensors
Interoceptive
  Internal data
  Battery voltage, failure detection

## Slide 10: Sensor Classification
Active
  Transmit signal into environment
  Sense return signal
  Radar, sonar
Passive
  Sense signal already available from environment
  Contact switch, compass, camera

## Slide 11: Sensor Classification
Absolute
  Zero position has physical meaning
  Absolute encoder, Compass, Accelerometer
Relative
  Zero position is just an arbitrary starting value
  Incremental encoder, Gyro heading

## Slide 12: Sensor Classification – MediumUsed
Electromagnetic radiation
Vibrations
Chemical concentration
Physical contact

## Slide 13: What is Sensing?
Collect information about the world
Sensor: an electrical/mechanical/chemical device that maps an environmental attribute to a quantitative measurement
Each sensor is based on a transduction principle - conversion of energy from one form to another
Also known as transducers

## Slide 14: Sensing Definitions
Resolution (Çözünürlük): Minimum difference that can be detected
Linearity: Sensor input/output variation is linear
Frequency/Bandwidth: # of reading per second
Range
Accuracy (Doğruluk)
Precision (Hassasiyet)
Repeatability
Sensitivity:

## Slide 15: Touch Sensor – Limit Switch
Converts Sense of Touch to a code
Detects presence or absence of something
Used to mark a limit for movement
Flipper size determines detection range
NO: normally open, NC:normally closed
Pull-up resistor required for floating input

## Slide 16: Tilt Sensor
Cylindirical cavity + conductive free mass

## Slide 17: Bend Sensor
a variable resistor
resistance changes as it bends
assuming constant current, the measured voltage changes with resistance

## Slide 18: Bend Sensor - Problem
Using a bend sensor 100s when straight and 1000s when bent, what is the min and max current that is drawn, given 5V source?

## Slide 19: Light Sensor
photo-resistor
resistance changes with light intensity

## Slide 20: Temperature Sensor
thermal resistor “thermistor”
resistance changes with temperature

## Slide 21: Potentiometer
rotational sensor
resistance changes with position of dial

## Slide 22: Rotary Encoders
Converts Angular Position of a Shaft to a code
Measures how far a shaft has turned
Measurement can be used for distance and speed
One turn can be divided into 1000 or more counts
May output small voltage or digital code
Incremental or absolute type

## Slide 23: Rotary Encoders
Incremental Encoder, Absolute Encoder

## Slide 24: Rotary Encoders
Absolute Encoder measures angular position
Incremental Encoder measures change in position

## Slide 25: Rotary Encoders- Problem
Using a rotary incremental encoder with 16 counts per revolution on a motor shaft that drives a wheel with 10 cm diameter
  How far does the wheel travel for 1 encoder count?
  What should be the wheel diameter to be able to achieve 1cm/count resolution?
  How many counts are there per meter of travel for 10cm diameter wheel case?

## Slide 26: Rotary Encoders- Problem

## Slide 27: Compass
Measures magnetic field strength
If there is no disturbance Earth’s magnetic field is the strongest
Types:
  Hall Effect Compass
    Measures magnetic field’s effect on semiconductor
  Flux Gate Compass
    Phase difference between two perpenicular coils wound on aferrite

## Slide 28: Gyroscope
Measures the Angular Rate of Rotation
  Measures how fast the sensor is turning, degrees/sec
  Actual turn angle (Heading), is obtained by integrating the rate
Rate Gyros sense in one or more Axes
Types:
  MEMS based vibrating structure
  Optical gyroscope

## Slide 29: Accelerometer
Measures proper acc.: sense force of gravity and change in velocity
Can sense acceleration in one or more axes
Can be used for balancing, sensing vibration, measuring incline/orientation, collision detection
MEMS based spring mass damper system

## Slide 30: Inertial Measurement Unit (IMU)
Device that uses gyroscopes and accelerometers to estimate the relative position, velocity, and acceleration of a moving vehicle

## Slide 31: Global Positioning System
Each satellite continuously transmits data that indicate its location and the current time
GPS receivers are completely passive
Arrival time differences of transmission of two or more satellites inform the receiver its relative distance to each satellite
Satellites needed to be well synchronized

## Slide 32: Time-of-flight Active Ranging
Makes use of the propagation speed of sound or an electromagnetic wave
d: distance, c: speed of wave propagation, t: time of flight
Sound speed: 0.3 m/ms
Light speed: 0.3 m/ns

## Slide 33: Ultrasonic Sonar Sensor
SONAR is SOund Navigation and Ranging
Speed of sound in air depends on temperature and gas consantration
Ultrasound is sound above Human Hearing >20kHz
Measures how far an object is by Time-of-Flight
  Sends out a sound wave
  Times until the reflection returns

## Slide 34: Ultrasonic Sonar Sensor
Advantages
Reliable with good precision
Not as prone to outside interference
Good maximum range
Inexpensive
Disadvantages
Sensetive to smoothness
Sensetive to angle to obstacle
Poor resolution
Prone to self-interference (self echo)
Cannot detect too close obstacles
Soft surfaces absorb sund energy

## Slide 35: Laser Rangefinder
Most accurate sensors for measuring distance
Light is emitted and detected
Sensors are called LIDAR (LIght Detection And Ranging)

## Slide 36: Laser Rangefinder - Phase-Shift Measurement
(c: speed of light, f: frequency, : wavelength)
distance difference between transmitted and emitted light is 2D
Light travels at phase difference, so for phase difference total of distance is covered

## Slide 37: Laser Rangefinder
Advantages
Better resolution than US, IR, camera
Very reliable
Not as sensitive to lighting conditions as camera and IR
Disadvantages
Cannot ideftify mirrors, glass
More expensivethan all other sensors
Larger and heavier than all other sensors

## Slide 38: 3D Laser Rangefinder
Laser scanner that acquires scan data in more than a single plane

## Slide 39: Time-of-flight Camera
3D scene is captured at one time
There are no moving parts
Uses modulated infrared light source to determine the distance for each pixel
Typically covers ranges from 0.5 m up to 8 m
The distance resolution is about 1 cm
Typical images sizes are quite small: ZCAM 320x240, Swiss Ranger SR3000 174x144

## Slide 40: Triangulation Active Ranging
Use geometric properties measuring distance
If the receiver measures the position of the reflection along a single axis  1D sensor
If the receiver measures the position of the reflection along two orthogonal axes  2D sensor (structured light sensor)

## Slide 41: Optical Triangulation (1D sensor) – Infrared Range Sensor
Emit light from IR LED
Light is reflected from object
Receiver senses the angle at which the reflected light is returned
Receiver has a lens and CCD (Charge-coupled device) array

## Slide 42: Optical Triangulation (1D sensor) – Infrared Range Sensor
Advantages
Reliable with good precision
Small beam angle
Inexpensive
Disadvantages
Sensitive to smoothness
Sensetive to angle to obstacle
Short range
Prone to interference from ambient light
Cannot detect glass, mirror, shiny surfaces

## Slide 43: Structured Light (2D sensor)
Kinect

## Slide 44: Motion/Speed - Doppler Effect Sensing
Radar or sound
Measured frequency () at the receiver is a function of the relative speed () between transmitter and receiver where transmitter emits an EM or sound wave with frequency
(c:speed of wave)

## Slide 45: Omnidirectional Camera

## Slide 46: Stereo Camera

## Slide 47: Problem: Sensor Choice
What sensors to employ ?
mapping
  ranging - laser, sonar, IR, stereo camera pair
  salient feature detection - doors using color
Factors
  accuracy, cost, information needed etc.

## Slide 48: Problem: Sensor Placement
Where do you put them ?
  On/off board (e.g. localization using odometry vs. localization using beacons)
If onboard - where ?
  Reasonable arrangements – heuristic
  Optimal arrangements – mathematically rigorous

## Slide 49: Common Sensors for Mobile Robots
Contact sensors: Bumpers
Internal sensors
  Accelerometers (spring-mounted masses)
  Gyroscopes (spinning mass, laser light)
  Compasses, inclinometers, IMU (earth magnetic field, gravity)
Proximity sensors
  Sonar (time of flight)
  Radar (phase and frequency)
  Laser range-finders (triangulation, tof, phase)
  Infrared (intensity)
Visual sensors: Cameras
Satellite-based sensors: GPS

## Slide 50
PR2 Robot Sensors